## Slide 1: Week 5
Physical Layer : Wireless Networks

## Slide 2: Outline
History
Benefits
Time/frequency domain concepts
802.11 standards
802.11 Mac algorithm
Summary
Conclusion

## Slide 3: History
1880: Hertz discovered electromagnetic waves
1898: First commercial radio data service
1921: First Mobile Radio
1946: First Mobile Telephone Service In St. Louis by AT&T. Half-duplex
1970: First Cellular Phone Service In Chicago by AT&T w cell, handoff, and roaming
1971: First Wireless Data Network Aloha at University of Hawaii
1990: First Commercial Wireless LAN Product AT&T WaveLAN
1997: First Wireless LAN Standard - IEEE 802.11 2Mbps

## Slide 4: Wired Vs. Wireless Communication
Wired | Wireless
Each cable is a different channel
One media (cable) shared by all
Signal attenuation is low
High signal attenuation
No interference
High interference
noise; co-channel interference; adjacent channel interference

## Slide 5: Benefits

## Slide 6
-Reduced manufacturing complexity
-Reduced weight
-More reliable – less physical connections
-Easier to maintain / modify after production
-Any other?
Benefits of Wireless
Airbus A319 wiring loom (from www.lia-tech.com)
Notes: Airbus pic. Need details

## Slide 7: Why go wireless ?
Advantages
  Sometimes it is impractical to lay cables
  User mobility
  Cost
Limitations
  Bandwidth
  Fidelity
  Power
  (In) security

## Slide 8: Some facts
1.35 Billion mobile subscribers vs 1.2 Billion Fixed line subscribers at the end of 2003

## Slide 9: IEEE top 10 downloads

## Slide 10: Issues

## Slide 11: Issues
Security
Higher data rates (60GH ???)
Multiple In Multiple Out (MIMO) antennas: IEEE 802.11n
Seamless Networking ⇒ Handoff (IEEE 802.21)
Multimedia over Wireless: Media center extenders , VOIP/Video over cell phones
Channel congestion in license-exempt band

## Slide 12: Applications - LAN Extension
Saves installation of LAN cabling
Eases relocation and other modifications to network structure
However, increasing reliance on twisted pair cabling for LANs
  Most older buildings already wired with Cat 3 cable
  Newer buildings are prewired with Cat 5e or 6
Wireless LAN to replace wired LANs has not happened
In some environments, role for the wireless LAN
  Buildings with large open areas
    Manufacturing plants, stock exchange trading floors, warehouses
    Historical buildings
    Small offices where wired LANs not economical
May also have wired LAN
  Servers and stationary workstations

## Slide 13: Single Cell Wireless LAN Configuration

## Slide 14: Multi-Cell Wireless LAN Configuration

## Slide 15: Applications – Cross-Building Interconnect
Connect LANs in nearby buildings
Point-to-point wireless link
Connect bridges or routers

## Slide 16: Applications - Nomadic Access
Link between LAN hub and mobile data terminal
  Laptop or notepad computer
  Enable employee returning from trip to transfer data from portable computer to server
Also useful in extended environment such as campus or cluster of buildings
  Users move around with portable computers
  May wish access to servers on wired LAN

## Slide 17: Infrastructure Wireless LAN

## Slide 18: Applications – Ad Hoc Networking
Peer-to-peer network
Set up temporarily to meet some immediate need
E.g. group of employees, each with laptop or palmtop, in business or classroom meeting
Network for duration of meeting

## Slide 19: Add Hoc LAN

## Slide 20: Wireless LAN Requirements
Same as any LAN
  High capacity, short distances, full connectivity, broadcast capability
Throughput: efficient use wireless medium
Number of nodes:Hundreds of nodes across multiple cells
Connection to backbone LAN: Use control modules to connect to both types of LANs
Service area: 100 to 300 m
Low power consumption:Need long battery life on mobile stations
  Mustn't require nodes to monitor access points or frequent handshakes
Transmission robustness and security:Interference prone and easily eavesdropped
Collocated network operation:Two or more wireless LANs in same area
License-free operation
Handoff/roaming: Move from one cell to another
Dynamic configuration: Addition, deletion, and relocation of end systems without disruption to users

## Slide 21: Technology
Infrared (IR) LANs: Individual cell of IR LAN limited to single room
  IR light does not penetrate opaque walls
Spread spectrum LANs: Mostly operate in ISM (industrial, scientific, and medical) bands
  No Federal Communications Commission (FCC) licensing is required in USA or Ofcom in UK
Narrowband microwave: Microwave frequencies but not use spread spectrum
  Some require FCC licensing

## Slide 22: Infrared LANs Strengths and Weaknesses
Spectrum virtually unlimited
  Infrared spectrum is unregulated worldwide
  Extremely high data rates
Infrared shares some properties of visible light
  Diffusely reflected by light-colored objects
    Use ceiling reflection to cover entire room
  Does not penetrate walls or other opaque objects
    More easily secured against eavesdropping than microwave
    Separate installation in every room without interference
Inexpensive and simple
  Uses intensity modulation, so receivers need to detect only amplitude
Background radiation
  Sunlight, indoor lighting
  Noise, requiring higher power and limiting range
  Power limited by concerns of eye safety and power consumption

## Slide 23: Spread Spectrum LANs Hub Configuration
Usually use multiple-cell arrangement
Adjacent cells use different center frequencies
Hub/AP is typically mounted on ceiling
  Connected to wired LAN
  Connect to stations attached to wired LAN and in other cells
  May also control access
    IEEE 802.11 point coordination function
  May also act as multiport repeater
    Stations transmit to hub and receive from hub
  Stations may broadcast using an omnidirectional antenna
    Logical bus configuration
Hub may do automatic handoff
  Weakening signal, hand off

## Slide 24: IEEE 802.11 Architecture

## Slide 25: 802.11 Physical Layer
Issued in four stages
First part in 1997
  IEEE 802.11
  Includes MAC layer and three physical layer specifications
  Two in 2.4-GHz band and one infrared
  All operating at 1 and 2 Mbps
Two additional parts in 1999
  IEEE 802.11a
    5-GHz band up to 54 Mbps
  IEEE 802.11b
    2.4-GHz band at 5.5 and 11 Mbps

## Slide 26: Spectrum

## Slide 27: Electromagnetic Signal
Function of time
Can also be expressed as a function of frequency
  Signal consists of components of different frequencies
Notes: EM signal is used as a means to transmit information. EM is a function of time but it can also be expressed as a function of frequency
That is the signal consists of components of frequencies. However, the frequency domain view of a signal is more important.

## Slide 28: Concepts Related to Channel Capacity
Data rate - rate at which data can be communicated (bps)
Noise - average level of noise over the communications path
Error rate - rate at which errors occur
  Error = transmit 1 and receive 0; transmit 0 and receive 1

## Slide 29: Rule of thumb
As we select higher frequency for TX the Channel Capacity increases
As the frequency increases the EMW starts behaving as light
At higher frequency radio cannot penetrate walls , fog etc (60GHz)
The larger the antennas the long distance it will travel

## Slide 30
IBM 60 GHz chip with integrated dipole antenna
Example 60 GHz?
High bandwidth / channel re-use

## Slide 31: CSMA/CA
Listen before talk
4 way handshake

## Slide 32: IEEE 802.11 Protocol Architecture

## Slide 33: IEEE 802.11 Medium Access Control Logic

## Slide 34: IEEE 802.11 MAC Timing Basic Access Method

## Slide 35: 802.11?
802.11 e .....QoS multimedia
802.11h.......dynamic channel selection
802.11i.......Security
802.11n.......Enhanced throughput
802.11p....... Inter-vehicle and vehicle-road side communication at 5.8GHz
802.11s: Mesh Networks

## Slide 36: Bluetooth
Sony ericson
Danish king...blue tooth...found of blueberries
Later Intel , Nokia and Ericson joined in 1998
IEEE 802.15.1
2.4GH
10m
1Mb/s new version is 3Mb/s
Key Feature
  Low power
  Cheap
  V small 9 mm2

## Slide 37: Piconnet
Network formed by bluetooth
1 master and 6 slaves
Slaves are polled by master for TX

## Slide 38: Other IEEE Standards I
IEEE 802.16: Broadband Wireless Access / WirelessMAN / WiMax
  - wireless distribution system, e.g., for the last mile, alternative to DSL
  - 75 Mbit/s up to 50 km LOS, up to 10 km NLOS; 2-66 GHz band
  - initial standards without roaming or mobility support
  802.16e adds mobility support, allows for roaming at 150 km/h

## Slide 39: Other IEEE Standards III
IEEE 802.21: Media Independent Handover Interoperability
  standardize handover between different 802.x and/or non 802 networks

## Slide 40: Femtocell

## Slide 41
Questions