## Slide 1: Week 3 Lecture 3 and 4
Network Design

## Slide 2: Network Design

## Slide 3: Topology
A branch of mathematics concerned with those properties of geometric configurations that are unaltered by elastic deformations such as stretching or twisting
A term used in the computer networking field to describe the structure of a network
The cisco three tier model is a logical topology of the network.
The network blueprint.

## Slide 4: How Do You Know When You Have a Good Design?

## Slide 5: How Do You Know When You Have a Good Design?
When you already know how to add a new building, floor, WAN link, remote site, e-commerce service, and so on
When new additions cause only local change, to the directly-connected devices
When your network can double or triple in size without major design changes
When troubleshooting is easy because there are no complex protocol interactions to wrap your brain around
Notes: Said by Dr. Peter Welcher, consultant and author of many networking articles in magazines, etc.

## Slide 6: Top-Down Network Design
Network design should be a complete process that matches business needs to available technology to deliver a system that will maximize an organization’s success.
  In the LAN area it is more than just buying a few devices.
  In the WAN area it is more than just calling the phone company.

## Slide 7: Two Scenarios for design
Existing Network Infrastructure(NI)
New Network Infrastructure

## Slide 8: Working with Existing NI
When working on existing network consider the following
  Some changes will impact the entire network?

## Slide 9
For example: Improving the efficiency of network addressing or routing protocol changes
Integrating new security measures
Adding new network services, such as voice traffic

## Slide 10: Working with Existing NI
Impacting a Portion of the Network

## Slide 11
  Improving Internet connectivity and adding bandwidth
  Updating access layer LAN cabling
  Providing redundancy for key services
  Supporting wireless access in defined areas
  Upgrading WAN bandwidth

## Slide 12: Top-Down Network Design Steps
Analyze requirements
Develop logical design
Develop physical design
Test, optimize, and document design
Monitor and optimize network performance
Implement and test network

## Slide 13: Network Design Steps
Phase 1 – Analyze Requirements
  Analyze business goals and constraints. How?
  Analyze technical goals and tradeoffs
  Characterize the existing network if any
  Characterize network traffic

## Slide 14: Network Design Steps
Phase 2 – Logical Network Design
  Design a network topology (Today)
    Design models for addressing and naming.
    Why is it important?
    Select switching and routing protocols
    Develop network security strategies
    Develop network management strategies

## Slide 15: Network Design Steps
Phase 3 – Physical Network Design
  Select technologies and devices for campus networks
  Select technologies and devices for enterprise networks

## Slide 16: Network Design Steps
Phase 4 – Testing, Optimizing, and Documenting the Network Design
  Test the network design & how?
  Optimize the network design how?
  Document the network design & why?

## Slide 17: Business Constraints
Budget
Staffing
Schedule
Politics and policies

## Slide 18: Making Tradeoffs
Scalability 20
Availability 30
Network performance 15
Security 5
Manageability 5
Usability 5
Adaptability 5
Affordability 15
Total (must add up to 100) 100
You will always face constraints while designing the network. Depending upon situations you will have to adjust this table

## Slide 19: Cisco Three Tier Model
Originally applied to switched networks
Now apply to all different kinds of networks

## Slide 20: When to use it?
Small company.. Approx. 30 nodes one branch office?

## Slide 21: Why Use a Hierarchical Model?

## Slide 22: Why Use a Hierarchical Model?
Reduces workload on network devices
  Avoids devices having to communicate with too many other devices (reduces “CPU adjacencies”)
Constrains broadcast domains
Enhances simplicity and understanding
Facilitates changes
Facilitates scaling to a larger size

## Slide 23: Cisco’s Hierarchical Design Model
A core layer of high-end routers and switches that are optimized for availability and speed.
A distribution layer of routers and switches that implement policies and segment traffic
An access layer that connects users via hubs, switches, and other devices

## Slide 24: Question
What happens if we implement policies at the core layer?

## Slide 25: Network Topology Design Themes
Hierarchy
Redundancy
Modularity
Well-defined entries and exits

## Slide 26: Hierarchical Network Design
Enterprise WAN
Backbone
Campus A
Campus B
Campus C
Building C-1
Building C-2
Campus C Backbone
Core Layer
Distribution Layer
Access Layer
              Image from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 27: Flat Versus Hierarchy
Flat Loop Topology
Headquarters in Medford
Grants Pass Branch Office
Ashland Branch Office
Klamath Falls Branch Office
Headquarters in Medford
Ashland Branch Office
Klamath Falls Branch Office
Grants Pass Branch Office
White City Branch Office
Hierarchical Redundant Topology
              Image from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 28: Flat Topology

## Slide 29: Mesh Designs
Partial-Mesh Topology
Full-Mesh Topology
              Image from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 30: A Partial-Mesh Hierarchical Design
Headquarters (Core Layer)
Branch Offices (Access Layer)
Regional Offices (Distribution Layer)
              Image from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 31: Avoid Chains and Backdoors
Core Layer
Distribution Layer
Access Layer
Chain
Backdoor
              Image from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 32: 99.999% Availability May Require Triple Redundancy
Enterprise
ISP 1
ISP 2
ISP 3
Can the customer afford this?
This slide is not meant to be a design recommendation. Its for the purpose of discussion
              Image from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 33: Availability Downtime in Minutes
4.32
1.44
.72
.01
30
10
5
.10
1577
99.70%
526
99.90%
263
99.95%
5
99.999%
Per Hour
Per Day
Per Week
Per Year
.18
.06
.03
.0006
.29
2
105
99.98%
.012
              Table from top down network design 2nd ed by Priscilla Oppenheimer

## Slide 34: Triple redundancy ?

## Slide 35: Conclusion

## Slide 36: Reference
    Top-Down Network Design 2nd edition
              By Priscilla Oppenheimer